## Slide 1: 異なる親和性でのPt/n-アルカン界面の 界面熱抵抗と表面液体構造の相関
0
○Qing-Yao Luo, Donatas Surblys, Hiroki Matsubara, Taku Ohara
日本機械学会熱工学コンファレンス2022
Oct. 8th, 2022
Ohara Lab., Institute of Fluid Science, Tohoku Univ.
Surface Liquid Structure Correlation with Interface Thermal Resistance of Pt/n-alkane Interface at Different Affinities

## Slide 2
Background
Thermal interface material (TIM) fills the air–gap
©mccourier
ITR is introduced
ITR is decreased
Air
TIM
interface thermal resistance
size of semiconductors
ρ of heat dissipation
significance of ITR
Understanding the thermal transport mechanism at the interface of
solid-TIM at nano scale is essential
Billions transistors in one chip

## Slide 3
merits of polymer-based TIM
Background
mechanical properties
electronic properties
chemical properties
design flexibility
low price
conformability
TIM categories
only highly conductive polymer
polymer matrix + filler
polymer + nanocomposites
liquid metal
1D/2D materials
polymer-based TIM

## Slide 4
Existing Research on ITR of SLS System
Au-Ar-Au system
work of our group
at low η: ITRlarge pitch>ITRsmall pitch
at high η: ITRrough surface>ITRflat surface
at η close to 1: highly ordered liquids increase ITR
Surblys D, et al. J. Chem. Phys. 150, 114705 (2019)
work of others
Frank M, et al. J. Chem. Phys. 151, 134705 (2019)
Ag-Ar-Ag system
Same fractal dimension and depth of roughness have same ITR and liquid density profiles.
Increase roughness won’t be helpful to decrease ITR at high η.
ITR of polyatomic systems should be investigated even they are much more complex.

## Slide 5
Existing Research on ITR of SLS System
Au-Ar-Au system
work of our group
at low η: ITRlarge pitch>ITRsmall pitch
at high η: ITRrough surface>ITRflat surface
at η close to 1: highly ordered liquids increase ITR
Surblys D, et al. J. Chem. Phys. 150, 114705 (2019)
work of others
Frank M, et al. J. Chem. Phys. 151, 134705 (2019)
Ag-Ar-Ag system
Same fractal dimension and depth of roughness have same ITR and liquid density profiles.
Increase roughness won’t be helpful to decrease ITR at high η.
ITR of polyatomic systems should be investigated.
Aim of this work:
Investigating surface liquid structure correlation with interface thermal resistance of Pt/n-alkane (TIM)/Pt systems at different affinities

## Slide 6
480K
540K
Simulation Systems
Side view of Pt-C8H18-Pt system
pitch length:
0
19.575005 Å
117.45003 Å
polymer chain-length:
8, 16, 24, 32
19.575005 Å
pitch 19.6
pitch 117.5
Lx=Ly=117.45 Å
210 Å < Lz < 340 Å
Nunited-atom = 43200

## Slide 7
Simulation Setting
Potential models
Simulation periods

## Slide 8
Results
ITR at η of 0.1

## Slide 9
Conclusion
ITR at η of 0.1